CompuPhase
Packages

# Introduction
Packages is a tool to maintain a repository of packages of electronic components. It is developed with the goal that various applications use one and the same repository as a basis for their handling of packages. The repository is in a well-documented JSON format, easy to parse in a variety of programming languages.
Many packages for electronic components exist, but it is not as straightforward as having a long list. On occasion a package name refers to a group of packages, and package name on its own is not conclusive about all dimensions of the package. Essentially the same package may also be known under multiple names —this is in part the result of various standardization bodies that each on their own standardize packages, without regard to the other organizations doing the same.
EDA suites (Electronic Design Application) focus on a flattened view of the package: the footprint. For mechanical design, the height of the package is important too, and pick-&-place machines often need to know the shape of the terminals (for example, gull-wing versus lug-lead) to recognize and centre the component on the nozzle. That is to say: these various applications all use package data, but they don’t all need the same data. Packages groups the data in a structured way, and makes it easily searchable (using both keyword search and parametric search).
This manual starts with instructions on how to use and navigate the user-interface of the program. It then follows up with a chapter on the subject itself: the packages for electronic components. To use Packages well, both chapters are equally important, and you will find these two chapter to cross-reference each other.
The remaining chapters are reference material.
## License
The Packages application including its data set and other resources, hereby collectively referred to as “the software”, is copyright © 2021-2022 CompuPhase, and licensed under the Apache License version 2.
This manual is copyright © 2021-2022 CompuPhase and licensed under the Creative Commons Attribution-Non-Commercial-ShareAlike 4.0 International License.
The project is maintained at: https://github.com/compuphase/Packages
# Quick start
Packages is a Java application, using JavaFX for the user-interface. As such, it is a cross-platform application. In addition to the core application itself, there are separate downloads for Microsoft Windows and Linux that include a launcher or shell script, for easier installation.
## Installation
Packages requires Java JDK 1.7 or later. If you do not already have this JDK on your workstation, you need to install it separately (or choose an install that bundles the JDK).
In Microsoft Windows, run the installer. The application includes an example database. In case you install the application in the “Program Files” directory, and you are not running the application with administrator privileges, that database will be readable, but not modifiable. You can, of course, copy the example database into another location.
In Linux, run the install.sh shell script after unpacking the archive in the temporary directory. If you run the script as a normal user, the application will be copied to “~/Packages” (so: in the home directory of the current user); when run as root (e.g. sudo), the application is copied to “/opt/Packages”. No example database is installed, but you can download it separately and move it into a directory of your choosing.
 MacOS is not officially supported, but in general Java applications run without change on MacOS.
## User interface
On start-up, Packages opens the repository that was most recently used. In practice, you will probably use a single repository for all your packages, but you can have several repositories and select the one to browse/edit in the “File” menu.
Changes or additions to the repository are saved automatically on switching to a new package or when closing the application. There still is a “Save” option in the File menu, if you wish to save your edits without changing to a different package.
The application shows a single package at a time. On the top row, you will find the navigation buttons (browse buttons), as well as menu and search buttons. Below that, the package information is split in three sections.
The first section gives the generic package information: its name (or identification), its body size, number of pins, pitch between the pins, terminal style (shape of the leads), and other characteristics.
Figure 1: User-interface, main view
The second section lists variants of the same “common shape” for the package. The variant adds the height of the package, the standard it conforms to (if any) and the presence of an exposed pad (or “thermal pad”) to the generic information. See topic Common names & variants on page 12 for the distinction between a generic package and a variant.
The third section gives detailed information about the footprint for the package: the shape and size of the pads, and the positions of these pads. As an aside, Packages does not generate footprints for any EDA program —that is not its goal. However, due to the open format of the output file, a third-party script can use the detailed information on the package and pads to generate these footprints.
On start-up, Packages shows the full list with all packages in the repository. You can restrict the range to a subset, based on keywords or specific package parameters (e.g. span, height, pin count). See topic Searching and filtering packages on page 8 for details.
## Adding, modifying and deleting packages
Depending on the package, not all data may be relevant. However, the top section (of the user-interface, see Figure 1) should always be completed.
### Names, description
A package may have more than one name —this is covered in detail in the topic Common names & variants on page 12. The names that refer to the generic “flat view” shape of the package, should be listed as names in the top section. Other applications can use these aliases to look up package information in the course of exchanging data: different programs used in electronics production may use different names for the same package. Applications can also use the aliases to translate all packages being entered into the system to a preferred naming convention.
In the case of “chip” packages, like 0603 and 0805, we recommend to include both the “imperial” name and the “metric” name for the package (in this case 1508 and 2012 respectively). As explained in Metric versus Imperial (page 28), conflicts arise for the smaller packages: for example, 0603 is a valid package label in both imperial and metric —but pointing to two very different packages. Since Packages does not allow for naming conflicts, our recommendation is to add an “M” suffix to the metric label: the equivalent for 0603 is 1508M, and 0805 is 2012M.
In general, we also suggest to put the preferred name(s) first in the list of names. When an application translates package names into a preferred naming convention, it typically picks the first “preferred name” that matches the chosen naming convention.
The description is optional, and contains general purpose text. The description is included in the search function, so you can use the description to include search terms that are not covered by the other fields.
### Characteristics
For SMD type packages (the focus of the Packages application and data file), the terminal field is an important parameter. For optical alignment, pick-&-place machines need to know at what elevation to scan the (body of the) component, and that depends on the lead shape. Therefore, packages that are identical apart from their terminal style, must be entered as separate packages. For example, SOD123 and SOD123F have gull-wing and lug-lead terminals respectively, and they are therefore separate packages —not variants.
The fields for the pin count and pitch are fairly self-explanatory (see also topic Pitch and spans on page 15 for the pitch dimension). An exposed-pad (or thermal pad) is seen as an attribute of a package, and it is typically not included in the pin count.
The tape packaging orientation is standardized for common parts (see chapter Normal orientations, page 22). For connectors or exotic packages, the tape orientation can be selected here. Tape packaging orientation is relevant only for components package is tape (on reel); for packages too big for tape packaging, leave this field at zero. Again, see chapter Normal orientations for details.
The relevance of the “polarized” field is that packages for polarized components are regularly oriented differently in tape packaging than those for non-polarized parts.
### Body size, lead-to-lead size
Body size and lead-to-lead size are also inherent characteristics of a package. These sizes allow for a tolerance, however (this tolerance can be looked up in the specifications of the respective packages). See Package dimensions and outlines (page 13) for details on the various “size” specifications of a package.
If a package does not have pins (terminals are either “endcap” or “no-lead”), the lead-to-lead size does not need to be filled in (it is by consequence identical to the body size).
### References
If a package is standardized by one or more normative institutions, the name of the standard and the name of the institution can be added here. These fields are informational; if your company uses internal standards, these can be added here as well.
### Related packages
If a package is related to a different package, the name of the other package can be added here. For example, the diode packages SOD123 and SOD123F are identical except for their pin shape (gull-wing versus lug-lead). It then makes sense to mark these packages as related to each other.
### Variants
The middle section in the user interface (see Figure 1 on page 4) is for the variants of the generic package. The generic package portrays a flattened view. For a long time, EDA programs needed no more that this representation. For assembly of the PCB, and for mechanical design (e.g. design of the enclosure), the height of the package also becomes an important parameter (and it is quite common that a generic package exists in different heights). This is why the details of various variants can be entered in a table. See the topic Common names & variants (page 12) for background information.
For example, an LQFP package and an TQFP package share all parameters (and they share it with the generic QFP package), except that LQFP is about 1.5 mm thick and TQFP about 1.0 mm.
Each variant must have a unique name, and the name of a variant may not conflict with any of the aliases for the generic package either. Names for variants may follow a standard or an ad-hoc convention —see also Package naming standards (page 27). If it is a standardized convention, you can indicate that convention on the row too. Doing so enables applications to translate between naming conventions.
For the “flat view” dimensions, Packages stores the nominal size and a tolerance from that nominal size. For the height, it uses a range: minimum height to maximum height. The motivation is that package standards also specify the height as a range; IPC-7351 only records a maximum height in its naming convention.
### Footprint
The bottom section of the user interface (Figure 1, page 4) has design parameters for the footprints. A single package may have multiple footprints. For example, the IPC-7351 standard defines footprints for Least, Nominal and Most spacing between components (less spacing allows for higher density). Some packages may also define an adjusted footprint for wave soldering (as opposed to reflow).
The majority of footprints use a single pad shape & size for most (or all) of the pins. Packages splits the pad shapes from the pad positions for a package. Thus, you often need to add only one or two pad shapes, even for packages with a high pin count.
In the pad shape specification, you can furthermore mark a pad as “exposed pad” (also called a thermal pad). A pad marked as such is then only valid for those variants that are also marked as having an exposed pad (in the “variants” section of Figure 1).
For example, for a HSOIC8 package (8-pin SOIC with 1.27 mm pitch and an exposed-pad):
- a variant for the package must be added, with an appropriate name (for example, SOIC8P127_495X600X175T330X240 according to IPC-7351, or HSOIC8‑3.8x4.95 according to ED-7303);
- in the column “exposed-pad”, a tick mark should be placed on the row for the variant;
- in the footprint section, a pad shape must be added with the size of the exposed-pad, and this pad must also have a tick mark in the column “exposed-pad” (this will have pad-id 2 for this example package);
- a pad with pin-id 9 (one more than the pin count of the package, so 9 for an SOIC8) must be added, and referencing pad-id 2.
The exposed pad is typically not included in the pin count (in the package characteristics, top section of Figure 1).
## Searching and filtering packages
You can open the search view by clicking the button “Search” (top right in Figure 1, page 4) or with the key combination Ctrl+F.
The search is on keywords ❶and/or specific package parameters ❷. Only exact matches are found for the pin count and the pitch, if these are set as search parameters. However, for the span, a 10% margin applies.
Next to jumping to a match (by double-clicking on the row in the “matches” list ❸), you can add one or more matches to a selection ❹. When a selection is active, the range of packages in the main view (Figure 1 on page 4) is restricted to the selection. Multiple disjoint searches can be added to a selection.
## Sharing and Multi-User Operation
Within a single site, multiple users can share the same repository, with some caveats. It basically involves installing Packages on individual workstations, but storing the repository on a network path that is shared by all users. The users then open the repository on the network path.
Packages has file sharing rules to serialize access to the repository when multiple users want to read from, or write to, the file at the same moment. And while a JSON file is a text-stream file, Packages handles package records as individual blocks of data. When two users edit different packages, both edits will be preserved —regardless of who saves last.
The caveat is that when two users edit the same package, the edits of one user will overwrite those of the other. There is currently no protection against this scenario.
Packages inserted (or modified) in one repository can also be exported, and subse­quently imported into another repository. The first step in exporting packages, is to create a selection, see section Searching and filtering packages. After that, you can export the selection through the File menu.
The export file is in the format of a repository, as described in chapter File format specification, page 17. It can be opened and edited in the Packages application, like any other repository.
When importing a file, conflicts may occur. Packages requires each package name (and alias) to be unique, and each variant name must be unique too. Any conflicts that arise must be resolved before the file can be imported (partially or fully).
The view for resolving import conflicts has three lists. The leftmost list contains the packages that do not conflict. Only these can be imported. Note that the button “Confirm imports” only imports the packages that have a tick in the rightmost column, so that you can do a partial import.
To the right of the “Non-conflicting” list, is the list with packages that do conflict. When you resolve all conflicts for a package, the package gets removed from the “Conflicting” list and inserted in the “Non-conflicting” list.
On selecting an item in the “Conflicting” list, the section at the right shows the names and aliases of the package, and the table below shows the variants of the package (if any). Conflicts may appear in either.
When names/aliases conflict, these have a yellow background. You may edit these names, so that they no longer conflict. The table for the variants has a column labelled “conflict” near the right with tick-marks for those variants that conflict. Note that the table lists both conflicting and non-conflicting variants. As stated above, when all variants are adjusted to be non-conflicting and non of the names/aliases are conflicting, the package is moved to the “Non-conflicting” column.
There is a final option for variants of a package with conflicting names: the variants may be merged to the existing package in the repository. For this function, select the variants by placing a tick in the rightmost column, and click on the button “Merge selected variants”. Only those variants will then be imported, and they will be stored as variants of the existing package.
Note that you can only place a tick-mark on variants that do not conflict. If a variant conflicts, you must rename it before merging.

# Package concepts
It is obvious that a specification for a component package needs to record the size, pin count, pitch, and a few other characteristics. And it needs to have a kind of label that uniquely identifies it. Yet, as you look at the user-interface of Packages, you will spot right-away that there are multiple, different, fields for the size of the package, as well as multiple “labels” that all uniquely point to the same package.
## Common names & variants
The QFP group of packages comprises ranges of with pin counts from 16 to 256 and pitches from 0.4 mm to 1.0 mm. With a chosen pin count and pitch, for example QFP32 with pith 0.5, the name still refers to a group of packages that all share the essential dimensions in the flat plane. There are variants, like LQFP which is about 1.5 mm thick as opposed to 2.8 mm nominally for the plain QFP (the “L” in LQFP stands for low-profile), or TQFP with a nominal height of 1.0 mm (“T” stands for thin). There are also variants with bumpers in the corners to protect the leads, but these bumpers are not included in the body size —so the core dimensions are still the same as for QFP.
All these variants (with the same pin count & pitch) share the same footprint, and have the same pitch and body & lead-to-lead sizes. Packages therefore groups them together in a single specification. The variants, are listed in that specification with their distinguishing attributes.
Regardless, even a package group may be known under different names. As already noted earlier, in part this is due to different standardization organizations writing their own standard for one and the same package; see chapter Package naming standards on page 27 for more information. Also note that standardization organizations tend to follow industry practice —the package exists before the standard gets written. Therefore, Packages allows you to add aliases for each common name (as well as adding variants).
See also the topic Metric versus Imperial on page 28 for another reason why a class is known under different names: sometimes a standardization organization cannot decide what is (or should be) the standard.
## Package dimensions and outlines
The size or bounding box of a package may refer to one of four dimensions, and each has its purpose.
The body size is, indeed, the size of the bounding box around the body excluding the pins. The lead-to-lead size is the bounding box including the pins. For packages that have no pins extruding from the sides of body (like QFN or BGA), the body and lead-to-lead sizes are the same. In the package data file (see chapter File format specification on page 17), the lead-to-lead size may be omitted in case it is equal to the body size.
Figure 2: Package sizes
The footprint contour (also called the footprint outline) is the bounding box around the footprint. With the SOT23-5 example in the picture above, the contour is wider than the lead-to-lead size, but not as high. The courtyard goes around the package, the leads and the footprint; this is always the biggest size.
Packages stores the body size, lead-to-lead size and footprint contour. The courtyard is not stored, because it is the envelope around the lead-to-lead size and the footprint contour (and it can therefore be derived from these dimensions).
The horizontal and vertical dimensions for body, lead-to-lead, spans and others depend on how the how the package is oriented: turn it by 90 degrees and the x & y swap places. Therefore, to properly specify the any dimensions of a package, we must first establish the normal orientation (or zero-orientation) of that package. See chapter Normal orientations (page 22) for the standardized normal orientations of packages.
### Calculating the courtyard
The body size, lead-to-lead size and footprint contours are recorded in the package data file, but the courtyard is not. The reason is that the courtyard is derived from both the lead-to-lead size and the footprint contour. So the courtyard does not need to be stored; it can be calculated from the other dimensions when needed.
In addition, whilst our definition of the courtyard has no clearance (the bounding box of the courtyard fits precisely around the component and the footprint), in practice an amount of clearance should typically be added. What that amount is, however, depends on the purpose and the precision of the manufacturing equipment.
When the origins for the lead-to-lead size and the footprint contour are zero (see the next section for the origin offset), the courtyard width is simply the larger value of the lead-to-lead width and the footprint width; likewise the courtyard height is the larger value of the lead-to-lead height and the footprint height.
When the origin of either the lead-to-lead size or the footprint contour are non-zero, however, an extra step is needed to calculate the minimum and maximum extents (both horizontally and vertically) of both bounding boxes.
For example, if the horizontal and vertical size of a bounding box (for either lead-to-lead size or footprint contour) are given by cx and cy, and its origin by xorg and yorg, then the equations below calculate the extents.
x_min=-{{cx} over 2} + x_org ~~~~~~~~~~ x_max={cx} over 2 + x_org newline y_min=-{{cy} over 2} + y_org ~~~~~~~~~~ y_max={cy} over 2 + y_org
After that, the xmin value for the courtyard is the smaller value of the xmin values for the lead-to-lead size and footprint contour, just as xmax for the courtyard is the larger value of either.
To express the courtyard in terms of a size and an origin offset, the equations are:
cx=x_max - x_min ~~~~~~~~~~~ cy=y_max - y_min newline x_org= {x_min + x_max} over 2 ~~~~~~~~~~ y_org={y_min + y_max} over 2
Any clearance can be added to cx and cy (assuming the same clearance must be added to all sides).
## Origin offsets
An essential concept for machine assembly of a PCB (with a pick-&-place machine) is the centroid: the centre of mass. A pick-&-place machine picks up the component at its centroid. The rationale is that pick-&-place machines use suction to hold the component “glued” to its nozzle, and the amount of suction is calibrated to the weight of the component. However, if a component is not in balance beneath the nozzle, it may “float” on the nozzle as the nozzle accelerates and decelerates in its movements from the feeder to the placement position. In other words, placement may then be less accurate.
For symmetric packages (the grand majority of packages), the centroid coincides with the geometric centre. For these, the origin offsets are zero, for the body, the lead-to-lead envelope and for the footprint contour. Otherwise, you need to specify the appropriate offsets of the geometric centre relative to the centroid.
In the above figure of a TO-252 package (also known as DPAK), the centroid is marked with the blue ⊕ symbol. When looking at the body of the TO-252 package, the centroid still falls on the geometric centre of the body —which is by design. For the lead-to-lead envelope, this is not the case: the geometric centre is offset to the left of the centroid. In the concrete case of the TO-252 package, the origin offset of the lead-to-lead envelope is X: -0.9 mm, Y: 0 mm.
Figure 3: Centroid and geometric offset
The figure omits a drawing of the footprint for this package, but an origin offset applies to the footprint contour as well (and, consequently, to the courtyard too).
## Pitch and spans
The pitch is the distance between two pins or pads on the same row. The span is the distance between pads of opposing rows. It is illustrated in Figure 4 with a footprint for the SOT23-5 package.
The pitch is an attribute of the package (the pitch of a footprint is necessarily the same as the spacing of the pins of the package), but the span depends on the footprint. Typically, the span (horizontal and/or vertical) is slightly smaller than the lead-to-lead size in the same direction, but there is no hard rule —it depends on the terminal style amongst others. A quad-row package has both a horizontal and a vertical span; these are the same for square packages, but different for a quad-row rectangular package.
Figure 4: Pitch and span (on a footprint)
A 2-pin surface-mount component typically has a span, but not a pitch. Through-hole 2-pin connectors form an exception, their pin distance is often specified as their “pin pitch”.

# File format specification
The package file is a JSON file with an array of “objects”, each object representing a package. The table below describes the fields for a single package. The file uses the UTF-8 character set.
Fields that are not relevant for a particular package may be omitted. For example, the “exposed-pad” field is irrelevant for a 2-pin “chip” package, and it is usually not recorded. Likewise, for packages with “endcap” or “no-lead” terminals, the lead-to-lead size is identical to the body size, and it is then sufficient to record the body size.
For fields that have an array type, if that array has no elements, the field may also be set to null. For example, when a package has no variants, the variants field may be set to null, rather than an empty array. Still, the preferred way to handle this case is to not include the variants field at all.
Field	Type	Description
date-modified	string	date and time stamp of the last update to the package, in the form YYYY-MM-DDTHH:MM:SS (the letter “T” is a literal; it is the separator between the date and the time).
names	array of strings	common names
description	string	optional brief description
type	string	“SMD” or “Through-hole”
pin-count	integer	number of pins or leads of the package
pitch	number	pin pitch in mm, if applicable
polarized	boolean	true or false (may be absent if irrelevant)
terminal	string	one of the following: “endcap”, “gull-wing”, “inward-L”, “lug-lead”, “J-lead”, “no-lead”, “ball”, “castellated” or “through-hole”
tape-orientation	integer	angle between packaging orientation (EIA-481D) and normative zero-orientation (IPC-7351), in degrees
body	object	body size (excluding pins) and centroid
cx, cy	number	nominal horizontal and vertical dimensions in mm
tol.x, tol.y	number	optional tolerance for the horizontal and vertical dimensions in mm
x, y	number	offset of the body centre from the centroid
lead-to-lead	object	“lead-to-lead” size and centroid (see Figure 2 on page 13)
cx, cy	number	lead-to-lead nominal horizontal and vertical dimensions in mm
tol.x, tol.y	number	optional tolerance for the horizontal and vertical dimensions in mm
x, y	number	offset of the shape centre from the centroid
references	array of objects	list of normative references
standard	string	name or identification of the reference
organization	string	organization that established the reference
related-packages	array of strings	names of other packages in the package file to which this package is related
variants	array of objects	list of specific variants of the common name
name	string	the (normative) name of the variant
standard	string	name of the standard or convention (current options are IEA metric, EIA imperial, IPC-7351, ED‑7303, or none)
height	object	the height range of the variant in mm
low	number	minimum height in mm
high	number	maximum height in mm
exposed-pad	boolean	whether this variant has an exposed-pad
notes	string	optional comment or notes
footprints	array of objects	list of footprints
type	string	one of “nominal”, “least” or “most”, according to the specification in IPC-7351
span	object	distance between pads in opposing rows (see Figure 4 on page 16)
cx, cy	number	distance in mm
contour	object	footprint contour and centroid (see Figure 2 on page 13)
cx, cy	number	contour horizontal and vertical dimensions in mm
x, y	number	offset of the contour centre from the centroid
pad-shapes	array of objects	list of unique pad shapes and sizes used in the footprint
pad-id	integer	sequence number of the pad shape definition
cx, cy	number	horizontal and vertical dimensions of the pad in mm
shape	string	one of “rectangle”, “round”, “roundedrect”, “obround”, “polygon” or “special”
pad-type	string	one of “standard”, “exposed” or “mechanical”
hole	number	diameter of the hole in the pad (applicable for through-hole packages)
x, y	number	offset of the pad origin relative to the pad’s geometric centre
pad-positions	array of object	list of the pad positions
pin-id	string	pin number or name; this field is encoded as a string (rather than an integer) because pins in grid arrays are labelled with a column/row scheme, like “A2” or “C5”.
pad-id	integer	reference to the pad shape for this pin
x, y	number	position of the pad origin, relative to the centroid position of the footprint
rotation	number	rotation of the pad shape, relative to the definition in the pad-shapes array

## Notes
For the pad shape, a square pad is stored as a “rectangle” shape; the cx and cy parameters will establish that it is square. The radius for the rounded corners of a “roundedrect” shape is not specified; in the scope of Packages, the intent is to flag the pad shape as an intermediate form between rectangle and obround.
The pin-id has a “string” type rather than “integer”, because pins of a ball-grid, pin-grid or land-grid array use a letter for the row and a number for the column; the pin at the top-left is A1, for example.
All coordinates assume that in the 2D projection, the Y-axis points upwards. This is in conformance with the Gerber standard. Some design programs use a downward Y-axis —a common convention in the early days of computing. Such programs should flip the sign on Y coordinates on reading the data from the JSON file.

Figure 5: X & Y axis orientation
# SMT terminal types
Name	Notes
endcap	used on 2-pin “chip” packages
gull-wing	common on semi­conductor packages, especially for components with more than two pins (this terminal shape is also called L-lead)
lug-lead	pins extend flat from the bottom, used on some diode packages (this terminal shape is also called flat-lead)
inward-L	used on 2-pin “molded” packages, such as tantalum capacitors (note how the pin folds underneath the package)
J-lead	components with J-lead terminals can be soldered on the PCB or be inserted in a socket / PLCC packages use J-lead extending from all four edges
no-lead	notably QFN, DFN and SON packages / on occasion, pads are “pulled back” from the edges (PQFN for Pulled-back, Quad Flat No-lead)
ball-grid
land-grid	similar to ball-grid, but flat contact surfaces instead of solder balls / may be used with a needle-pin connector, or be reflow soldered
castellated	common for modules, occasionally used on resistor arrays / on 2-pin components, this terminal style is also called side-concave

# Normal orientations
The normal orientation is the orientation that the component has when its rotation is zero degrees. There are two predominant standards for the normal orientation of components on a PCB. Fortunately, these two standards, IPC-7351 and IEC 61188‑7 “Level A”, are compatible with each other.
In brief, the normal orientation of 2-pin packages is such that pin 1 is on the left and pin 2 is on the right. For polarized components, such as electrolytic or tantalum capacitors, pin 1 is the “plus”-pin. For diodes, pin 1 is the cathode. For packages with more than 2 pins, the component is oriented as such that pin 1 is aligned to the top left corner. If pin 1 is in the middle of an edge, instead of near a corner, pin 1 must be aligned to the top. A few exceptions to these general rules are noted beneath the table.
Most surface mount components come packaged in tape, on reel. A separate standard exists for how the components are packaged in carrier tape, EIA-481. Manufacturers generally adhere to the EIA-481 standard, but many also specify exceptions for specific component packages; for example, many manufactures have continued to package QFP and QFN packages according to the rules in EIA-481C instead of adopting the changes of EIA-481D.
The table below shows the normal orientations according to IPC-7351 and the packaging orientation according to the latest EIA-481 standard. The angle by which a package must be rotated to go from EIA-481 to IPC-7351 is also given.
Note that EIA-481 only applies to packaging in tape; see the notes at the end of this section for tube and tray packaging.
EIA-481D		IPC-7351	Notes
			Non-polarized chip or moulded packages, e.g. resistors, capacitors, inductors, 2-pin crystals.
			Polarized chip or moulded packages (except capacitors, see below). For diodes, pin 1 is the cathode.
			Tantalum capacitors or other capacitors in moulded packages. Pin 1 (with a bar) is the positive pole.
			Electrolytic capacitors. Pin 1 is the positive pole. (The black bar marks the negative pole.)
			Power inductors (non-polarized).
			PLCC2 package (for LEDs). See also the notes below.
			PLCC4 and PLCC6 packages (for multi-colour LEDs). See also the notes below.
			Resistor arrays and capacitor arrays in a chip package.
			Ceramic resonators with 3 pins. See the notes below for crystals and oscillators with two or four pins.
			Rectangual 4-pin crystals. See the notes below for crystals with two pins, and oscillators with a square shape.
			3-pin SOT style transistor, e.g. SOT23, SOT323, SOT523, SC70, TO-236.
			5-pin SOT style packages, e.g. SOT23-5, SC70‑5, SSOP-5.
			6-pin & 8-pin SOT style packages, e.g. SOT23‑6, SC70-6, SSOP-6.
			SOT143 and SOT343.
			SOT223, SC73, TO-89, TO-261. (See below for similar packages.)
			SOT89, TO-293. (See above and below for similar packages.)
			DPAK D2PAK, TO-220, TO-252, TO-263. (See above for similar packages.)
			Rectangular IC packages: SOIC, SSOP, TSSOP, TSOP type 2 (but see below for TSOP type 1).
			TSOP type 1.
			Square IC packages: QFP, QFN, SON, DFN (but not BGA and most PLCC, see below).
			Square IC packages that have pin 1 in the middle of the row, which is common for PLCC packages.
			Square Grid array IC packages (BGA, LGA, PGA); see above for QFN, QFP and other square IC packages.

## Notes
### PLCC2, PLCC4 and PLCC6
The low pin count PLCC packages for LEDs have a chamfered corner to mark pin 1. For PLCC2, pin one is usually the cathode (conforming to IPC-7351); for RGB LEDs in PLCC4 and PLCC6 packages, pin 1 is typically the common anode.
The PLCC4 package uses a clockwise pin numbering scheme, starting from pin 1 in the upper left corner. The zero-orientation is not explicitly defined in the IPC-7351 standard (because IPC-7351 assumes a counter-clockwise pin numbering).
The PLCC6 package uses a counter-clockwise pin numbering scheme, similar to dual-line IC packages.
### Crystals, ceramic resonators, oscillators
Crystals in a 2-pin chip package follow the orientation of 2-pin non-polarized chip packages. Ceramic resonators with three aligned pins are oriented as shown in the table.
For crystals and crystal oscillators with four pins (or more), the orientation in tape is inconclusive. Rectangular shaped crystals generally follow the alignment as shown in the table. Square packages (which are typically oscillators, rather than crystals) regularly use the orientation of PLCC4.
4-pin crystals and oscillators may use a clockwise pin numbering, like PLCC4. For crystals, the pin numbering direction is mostly irrelevant, because the crystal is typically connected between pins 1 and 3 (with pins 2 and 4 either unconnected, or both connected to ground). Regardless of the direction of the pin numbering, pins 1 & 3 are at the same positions.
### Tube and tray orientations
Components are oriented sideways in tube (sticks), such that the pins of consecutive components do not touch. The end of the tube that “pin 1” of the component points to is often marked with a green stop or pin.
JEDEC trays have a chamfered corner. If the tray is oriented such that the chamfered corner is on the upper left, the components in the tray are oriented according to IPC-7351.
# Package naming standards
There have been several attempts to come to a generic naming convention that describes standard packages in a more precise and less ad-hoc way. The one that has gained widest acceptance, is IPC-7351B “Naming Conventions for Standard SMT Land Patterns”. This standard is not without its flaws, though: internal inconsistencies and ambiguous descriptions make the standard open to interpretation. These were set out to be fixed in the updated IPC-7351C standard, but the work on this update stalled, the IPC workgroup disbanded and the new workgroup has not held a meeting for the past four years.
A draft for the proposed updates for the chapter on the package naming convention, though, was published by the author of that chapter —the “Library Expert Footprint Naming Convention”. It is available from https://www.pcblibraries.com/, requiring a free registration. Despite being an unofficial standard, this draft document is considered the current IPC naming convention. For a summary, see topic IPC-7351 summary (page 29), and for examples see page 31.
A contender is JEITA standard ED-7303C “Name and code for integrated circuits package” (originally an EIAJ standard; JEITA is the successor of EIAJ). ED‑7303 is more limited than IPC-7351, because it only deals with packages for integrated circuits. The advantage, however, is that the naming convention stays closer to the industry-standard names like TSSOP and LQFP. Codes for pitch, span, or body sizes are affixed at the end as needed. See topic ED-7303 summary (page 30) for an overview and page 31 for examples.
Of mention is furthermore the JEDEC standard JESD30 “Descriptive Designation System for Electronic-device Packages”. This is an elaborate standard that tries to describe every feature of a package. The resulting package names are cryptic, though, and it does not appear that this standard is active use. Curious, in this respect, is that JEDEC also maintains a large collection of design drawings for electronic packages, categorized as a two-letter prefix plus a sequence number (plus an optional suffix), where the prefix is “DO” for diodes, “TO” for transistors, and “MO” or “MS” for integrated circuits. These drawings “reference labels” are actually in common use (e.g. DO‑219AA as an alias for SOD123, or TO‑252 as an alias for DPAK). Yet, JESD30 ignores these reference drawings and restarts from scratch.
Lastly, none of the above standards covers manufacturer-specific packages (and footprints), such as those for connectors, submodules and special components. As a result, there are no standard names for these packages either. The common convention is that these packages are named:
Manufacturer Name + “_” + Product Number
An example of the above convention is CUI_PJ-001AH-67. —a SMT mounted DC power connector manufactured by CUI.
The product number may contain wild-card characters (typically an “x”), in case there is a range of components that all use the same package.
### Metric versus Imperial
In the 1980s, the various standardization organizations for the electronics industry came to an agreement to move to metric and specify the dimensions in all future standards in millimetres. However, when the (USA-based) EIA published the PDP‑100 standard on the “chip” packages (for surface mount resistors, capacitors, ferrite beads and other 2-pin parts) in 1987, the backlash from the USA industry was such that the EIA back-pedalled on its decision and republished the standard a year later with dimensions in both imperial and metric.
The trouble is: the EIA also chose to identify the packages by their size. For example, the 0805 package is a chip with a length of 8/100th inch and a width of 5/100th inch. In other words, the package’s label is simply its dimensions in the 2D plane in increments of 0.01 inch. In metric, this size is roughly 2.0 × 1.25 mm. That same 0805 package can also be labelled 2012 —again the length and width of the package, but now in increments of 0.1 mm. Both 0805 and 2012 refer to the same package; both are valid, standardized names for one and the same package; both are in active use, although imperial is more common than metric (especially in the USA).
A complication is that you cannot tell from looking at the package name alone, whether it should be interpreted as imperial or metric. At this time, there does not exist a package with the imperial size of 2012, so in this case you can make an educated guess that 2012 must be interpreted as metric. However, conflicts do exist: 0603, 0402 and 0201 are valid imperial sizes for a package as well as a valid metric sizes —but the metric packages being more than twice as small as their imperial counterparts with the same moniker.
Imperial	Metric	Body size
008004	0201	0.25×0.125 mm
01005	0402	0.4×0.2 mm
0201	0603	0.6×0.3 mm
0402	1005	1.0×0.5 mm
0603	1608	1.6×0.8 mm
0805	2012	2.0×1.25 mm
1008	2520	2.5×2.0 mm
1206	3216	3.2×1.6 mm
1210	3225	3.2×2.5 mm
1808	4520	4.5×2.0 mm
1812	4532	4.5×3.2 mm
2010	5025	5.0×2.5 mm
2012	5032	5.0x3.2 mm

Common “chip package” sizes, in imperial and metric
There was some hope, roughly twenty years ago, that the schism between metric and imperial would be resolved, because the EIA suspended its yearly updates to the PDP-100 standard in 1995, due to it being “in revision”. It never materialized, though (and neither were the updates resumed). The EIA ceased its operations in 2011.
A convention that is increasingly applied (but not yet universal) is to add an “M” suffix to the metric specifications of the packages. Thus, we speak of 0805 and 2012M.
## IPC-7351 summary
IPC-7351 touts itself as a standard for “land patterns” (footprints), and it adds a suffix at the end of every footprint name to indicate the desired density of the assembly. A high density imposes a smaller footprint, and thus IPC-7351 identifies each package with three different labels for three standardized densities: Nominal, Least and Most —where “least” is for the footprint with the least spacing and the smallest pads, so for the highest density. In its label, the last letter (“N”, “L” or “M”) indicates the density. The density is not relevant for a package description, therefore this letter may be dropped on the package name or variant name.
Dimensions are in 1/100th of a millimetre. The X, Y and Z dimensions are separated with an “X”, and the “X” and “Y” dimensions refer to the lead-to-lead size. For the X and Y dimensions, the value is the nominal size; for the X dimension, the value is the maximum size. For example, a 20-pin TSSOP package (with standard 0.65 mm pitch) is named as SOP20P65_650X640X110. You can dissect this name as:
- package style = small outline with pins (“SOP”)
- 20 pins, pitch = 0.65 mm (65/100 mm)
- lead-to-lead size = 6.5×6.4 mm, max. height = 1.1 mm
However, for packages for discrete components, IPC-7351 switches to the (metric) convention of PDP‑100, which is 1/10th of a millimetre, and drops the “X” between the X and Y dimensions. For example, a common “chip” style resistor is RESC2012X50N, which we can dissect as:
- component type = resistor (“RES”)
- package style = chip (“C”)
- lead-to-lead size (same as the body size) = 2.0×1.2 mm, max. height = 0.5 mm
The inclusion of the component type in the package name leads to a proliferation of package/footprint specifications that all are essentially identical —the type of a component is neither relevant for the package, nor for the footprint.
## ED-7303 summary
ED-7303 limits itself to packages for integrated circuits. For discrete semi­conductors, JEITA suggests using the “SC” codes (separate JEITA standards). No guideline is given for discrete passive components, but EIA PDP‑100 is the obvious choice. However, that still does not solve the issue of metric versus imperial.
The recent ED-7303 standard specifies the package sizes in millimetres. These are plain millimetres, not scaled millimetres like in IPC-7351. Also in contrast to IPC‑7351 is that ED-7303 specifies the dimensions of the body of the package, rather than the lead-to-lead size. However, ED-7303 comes of age: the original specification is from June 1998, and it carries that history in the form of legacy notations that are now redundant and no longer recommended —yet still valid. This manual restricts itself to summarizing the recommended standard.
The height of the package is encoded in a prefix to the general package name. For example, VQFP is a QFP with a height between 0.8 mm and 1.0 mm; see the table below.
Code	Description	Seated height
L	Low profile	1.2 mm < L ≤ 1.7 mm
T	Thin	1.0 mm < T ≤ 1.2 mm
V	Very thin	0.8 mm < V ≤ 1.0 mm
W	Very very thin	0.65 mm < W ≤ 0.8 mm
U	Ultra thin	0.5 mm < U ≤ 0.65 mm
X	Extremely thin	X ≤ 0.5 mm

Other prefixes flag features like the presence of an exposed-pad (“H”), or bumpered corners (“B”). Multiple prefixes can be chained.
An example for a package code according to ED-7303 is P-HTSSOP24–7.8x4.4-0.65, which means:
- plastic body (“P-”)
- exposed-pad (“H”)
- thin (“T”), height between 1.0 mm and 1.2 mm
- package style = shrink small outline with pins (“SSOP”)
- 24 pins
- body size = 7.8×4.4 mm
- pitch 0.65 mm
  The material code (“P-” in the above example) is required according to the standard, but actually superfluous —so it is, in fact, often omitted.
## Examples of package names
IPC-7351C (draft) ❶	ED-7303C / JEITA	Description
RESC2012X50 ❷		0805 imperial, resistor, 2.0×1.25 mm, 0.5 mm high (max.)
CAPC1608X80 ❷		0603 imperial, capacitor 1.6×0.8 mm, 0.8 mm high (max.)
CAPMP3216X120 ❷		polarized capacitor in molded package (e.g. tantalum capacitor), 2.0×1.25 mm, 1.2 mm high (max.)
CAPAE660X610 ❷		aluminium electrolytic capacitor, case D, lead span 6.6 mm (body 6.3 mm), 6.1 mm high
BEADC2012X60 ❷		0805 imperial, ferrite bead, 2.0×1.25 mm, 0.6 mm high (max.)
INDM4240X350		power inductor in molded package, 4.2×4.0 mm lead-to-lead size, 3.5 mm high (max.)
RESCAV10P65_3216X50 ❷		0612-10 imperial, resistor array, 10 pins, 1.6×3.2 mm, 0.5 mm high
CFP6P65_2012X70		0508-6 imperial, ceramic flat package (6 pins), 1.25×2.0 mm, 0.7 mm high
DIOM5538X262 ❷		SOD132, DO-214AA
DIOMELF5025 ❷		SOD87, DO-213AB, MELF package
LEDC3216X110 ❷		LED in chip package (1206 imperial), may have a dome
SOD3816X110	SC-109D ❸	SOD123, DO-219AA
SOT6P65_210X110	SC-70-6 ❸	SOT363, MO-203AB
DPAK3P230_1000X230	SC-63 ❸	DPAK, TO-252
XTALDFN2520X50		4-pin crystal, no-lead, body 2.0×2.5 mm
SOP20P65_650X640X110 ❺	P-TSSOP20-6.5x4.4-0.65 ❹	TSSOP 20-pin, 0.65 mm pitch, 6.5×4.4 mm body size, 6.5×6.4 mm lead-to-lead, 1.1 mm height
SOIC8P127_495X600X175T330X240 ❺	P-HSOIC8-3.8x4.95 ❹	SOIC 8-pin with exposed-pad, 1.27 mm pitch, 3.8×4.95 mm body size, 6.0×4.95 mm lead-to-lead, 1.75 mm height
QFP48P50_900X900X110 ❺	P-TQFP48-7x7-0.50 ❹	QFP 48-pin, 0.5 mm pitch, 7×7 mm body size, 9×9 mm lead-to-lead size, 1.1 mm height

### Notes
❶	The last letter in an IPC-7351 “land pattern” name is a code for the footprint density. It is usually “N”, which stands for nominal, but may also be “L” (least) or “M” (most). It is not relevant for package names, and therefore has been omitted in these examples.
❷	IPC-7351 includes the component category in the name (CAP for capacitor, RES for resistor, etc), even though this is irrelevant for both the package and the footprint.
❸	JEITA ED-7303 standardizes only package codes for integrated circuits. For discrete components, the standard refers to separate JEITA standards, notably ED‑7500B.
❹	The first letter of a package name in ED-7303 indicates the material for the body, like “P” for plastic or “C” for ceramic. The standard asserts this prefix is mandatory; it is irrelevant for the package dimensions, however, and is frequently omitted.
❺	IPC-7351 uses the lead-to-lead size of a package, whereas ED-7303 uses the body size. Furthermore, for these packages, IPC-7351 changes its notation for the size.
# Package trivia
## SSOP versus TSSOP
SSOP is the abbreviation for “Shrink Small Outline Package”, and from the ED‑7303 standard we learn that the “T” in TSSOP stands for “thin”. However, these packages are different enough that they won’t fit on each other’s footprints.
SSOP was standardized by JEDEC (MO-137), as a dual-row package with gull-wing leads, a pitch of 0.025 inch and a body width of 0.15 inch. TSSOP was originally standardized by EIAJ (now JEITA), also as a dual-row package with gull-wing leads, but with a pitch of 0.65 mm and a body width of 4.4 or 5.3 mm. The difference in pitch is subtle, yet critical: 0.025 inch is 0.635 mm —versus 0.65 mm of TSSOP. The width is different too: 0.15 inch is rounded to 3.9 mm.
The similarity of the packages and their names has caused confusion: as the MO‑137 standard specifies only a maximum height, SSOP packages less than 1.2 mm high are sometimes referred to as TSSOP. This confusion could have been avoided, had JEDEC adopted the alternative name: QSOP. However, while some manufactures use it, the QSOP name is unofficial.
## BGA & LGA pin numbering
The pins in grid-array packages are identified by row and column. The row is indicated with a letter (or a sequence of two letters, when the number of rows exceeds 20); the column is indicated with a number. When viewed from the tip, the top-left pin is A1. The letters “I”, “O”, “Q”, “S”, “X” and “W” are skipped in the row numbering. The relevant JEDEC standard is SPP-010.